## Slide 1
CRYPTOGRAPHYv
REF.NO.
22_EC_19
[ DEPT. OF ELECTRONICS & COMMUNICATION ]
A FLEXIBLE FPGA APPROACH TO IMAGE
CRYPTOGRAPHY
Using PYNQ-Z2 — Xilinx Zynq-7000
Lagineni Sreenithai · Raghavendra S M · Chandrakiran S M · Mulukuri Vallesh Nath
Guide: Ms. Chaithra S

## Slide 2
SECTION
01 / 12
The Case for Hardware Encryption
Software AES on CPU cannot meet real-time multimedia demands.
PROBLEM & SOLUTION
THE PROBLEM
Explosive data growth
Medical scans, biometrics, surveillance, and satellite imagery traverse open networks continuously.
CPU bottleneck
Software AES/RSA on CPUs introduces high latency unusable for real-time telemedicine and live monitoring.
Security threats
Unauthorized access, data breaches, and malicious tampering are growing in severity.
OUR APPROACH
AES-128 on FPGA Fabric
Hardware-accelerated encryption via Vivado HLS, controlled through a Python software interface.
HARDWARE
FPGA Speed
SOFTWARE
Python Jupyter
BRIDGE
AXI DMA
TARGET
Low Latency
Dept. of Electronics and Communication— K.R. PURAM, BENGALURU

## Slide 3
SECTION
02 / 12
PYNQ-Z2 Board
ARM CORTEX-A9
Dual-core Processing System
FPGA FABRIC
Programmable Logic for HLS
ETHERNET / USB-UART
Network transfer & debug
MICRO SD
Linux boot image storage
HARDWARE PLATFORM
[ PYNQ-Z2 / ZYNQ-7000 ]
PROCESSING SYSTEM PS
ARM Cortex-A9
Image acquisition via Python
Pixel packing to 128-bit AES blocks
Image reconstruction post-decrypt
PROGRAMMABLE LOGIC — PL
FPGA Fabric
HLS Encryption IP core (Vivado)
Pipelined AES-128 hardware modules
DMA burst transfers (256–4096 bytes)
AXI-LITE
PS control signals: start/stop, key, IV
AXI-STREAM
High-speed pixel stream PS ↔ PL
AXI-DMA
Bulk image transfer from DDR to fabric
Dept. of Electronics and Communication— K.R. PURAM, BENGALURU

## Slide 4
SECTION
03 / 12
FPGA Advantage
Each round stage maps to a pipelined hardware module — parallel execution, minimal latency per block.
AES-128 ENGINE
ROUND 0
AddRoundKey
→
ROUNDS 1–9
Sub + Shift + Mix + AddKey
→
ROUND 10
Sub + Shift + AddKey
STEP 01
SubBytes
Non-linear S-box substitution — confusion
STEP 02
ShiftRows
Cyclic row shifting — inter-byte diffusion
STEP 03
MixColumns
Galois Field GF(2^8) matrix multiply
STEP 04
AddRoundKey
XOR with round-derived key — key mixing
BLOCK SIZE
128-bit
KEY LENGTH
128-bit
TOTAL ROUNDS
10
CIPHER TYPE
Symmetric
Dept. of Electronics and Communication— K.R. PURAM, BENGALURU

## Slide 5
SECTION
04 / 12
AES-128 ENCRYPTION PROCESS
Dept. of Electronics and Communication— K.R. PURAM, BENGALURU

## Slide 6
SECTION
05 / 12
AES-128 ENCRYPTION
Dept. of Electronics and Communication— K.R. PURAM, BENGALURU
SUB BYTES
SubBytes is a non-linear byte substitution step where each byte of the 4×4 state matrix is replaced using a fixed AES S-Box, introducing cryptographic confusion.
This operation is designed to resist linear and differential cryptanalysis by breaking simple mathematical relationships between plaintext and ciphertext.

## Slide 7
SECTION
06 / 12
AES-128 ENCRYPTION
Dept. of Electronics and Communication— K.R. PURAM, BENGALURU
SHIFT ROWS

## Slide 8
SECTION
08 / 12
AES-128 ENCRYPTION
Dept. of Electronics and Communication— K.R. PURAM, BENGALURU
MIX COLUMNS
MixColumns treats each column of the state matrix as a polynomial and multiplies it with a fixed constant Matrix.
This operation ensures strong diffusion, meaning a single input byte affects multiple output bytes across the column.

## Slide 9
SECTION
09 / 12
AES-128 ENCRYPTION
Dept. of Electronics and Communication— K.R. PURAM, BENGALURU
ADD ROUND KEY
AddRoundKey combines the current state matrix with the round key using a bitwise XOR operation, directly injecting key material into the data.
Since XOR is reversible, this step ensures secure key mixing while allowing correct decryption using the same round key.

## Slide 10
SECTION
10 / 12
ALL TIMING MET
Zero failing endpoints out of 41,536
WNS: 0.523 ns — all user-specified constraints satisfied.
VERIFICATION & RESULTS
FUNCTIONAL VERIFICATION
Encrypted output
Visually indistinguishable from random noise
Decrypted image
Perfect lossless restoration — pixel-exact match
TIMING SUMMARY
METRIC
VALUE
WNS
0.523 ns
TNS
0.000 ns
WHS
0.016 ns
Failing Endpoints
0 / 41,536
Total On-Chip Power
2.784 W
Dept. of Electronics and Communication— K.R. PURAM, BENGALURU

## Slide 11
SECTION
11 / 12
Future Directions
Optimize DMA burst behavior and reduce PS load.
Apply HLS/PL-level clock gating for power reduction.
Scale with additional parallel IP cores or multi-channel DMA.
CONCLUSION
DEMONSTRATED
Real-time AES-128 image encryption on PYNQ-Z2 FPGA
CO-DESIGN
PS handles control logic; PL handles raw cryptographic computation clean separation of concerns.
0
Failing endpoints
128
bit AES key & block
2.784W
Total on-chip power
57.1°C
Junction temp (safe)
Lagineni Sreenithai · Raghavendra S M · Chandrakiran S M · Mulukuri Vallesh Nath
Guide: Ms. Chaithra S | Department of Electronics & Communication Engineering

## Slide 12
SECTION
12 / 12
CONFERENCE SUBMISSION
Lagineni Sreenithai · Raghavendra S M · Chandrakiran S M · Mulukuri Vallesh Nath
Guide: Ms. Chaithra S | Department of Electronics & Communication Engineering